## Slide 1: A recap of congestion control in TCP
Based upon slides from:
D. Choffnes, P. Gill, S. Katti, and N. Carlsson (Linköping University, Sweden)
Bob Kinicki (Worcester Polytechnic Institute)
Bob Briscoe et al. (IETF 96 meeting)

## Slide 2: What is Congestion?
Load on the network is higher than capacity
  Capacity is not uniform across networks
    Modem vs. Cellular vs. Cable vs. Fiber Optics
  There are multiple flows competing for bandwidth
    Residential cable modem vs. corporate datacenter
  Load is not uniform over time
    10pm, Sunday night = Bittorrent Game of Thrones

## Slide 3: Why is Congestion Bad?
Results in packet loss
  Routers have finite buffers
  Internet traffic is bursty, no buffer can prevent all drops
  When routers get overloaded, packets will be dropped
Practical consequences
  Router queues build up, delay increases
  Wasted bandwidth from retransmissions
  Low network “goodput”

## Slide 4: Congestion Avoidance and Control Van Jacobson ‘88

## Slide 5: The Danger of Increasing Load
Knee – point after which
  Throughput increases very slow
  Delay increases fast
Cliff – point after which
  Throughput  0
  Delay  ∞
Congestion Collapse
Load
Load
Goodput
Delay
Knee
Cliff
Ideal point

## Slide 6: Cong. Control vs. Cong. Avoidance
Congestion Collapse
Goodput
Knee
Cliff
Load
Congestion Avoidance:
Stay left of the knee
Congestion Control:
Stay left of the cliff

## Slide 7: Advertised Window, Revisited
Does TCP’s advertised window solve congestion?
NO
The advertised window only protects the receiver
A sufficiently fast receiver can max the window
  What if the network is slower than the receiver?
  What if there are other concurrent flows?
Key points
  Window size determines send rate
  Window must be adjusted to prevent congestion collapse

## Slide 8: Goals of Congestion Control
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput

## Slide 9: General Approaches
Do nothing, send packets indiscriminately
  Many packets will drop, totally unpredictable performance
  May lead to congestion collapse
Reservations
  Pre-arrange bandwidth allocations for flows
  Requires negotiation before sending packets
  Must be supported by the network
Dynamic adjustment
  Use probes to estimate level of congestion
  Speed up when congestion is low
  Slow down when congestion increases
  Messy dynamics, requires distributed coordination

## Slide 10: TCP Congestion Control
Each TCP connection has a window
  Controls the number of unACKed packets
Sending rate is ~ window/RTT
Idea: vary the window size to control the send rate
Introduce a congestion window at the sender
  Congestion control is sender-side problem

## Slide 11: Congestion Window (cwnd)
Limits how much data is in transit
Denominated in bytes
wnd = min(cwnd, adv_wnd);
effective_wnd = wnd –
(last_byte_sent – last_byte_acked);
last_byte_acked
last_byte_sent
wnd
effective_wnd

## Slide 12: Two Basic Components
Detect congestion
  Packet dropping is most reliably signal
    Delay-based methods are hard and risky
  How do you detect packet drops? ACKs
    Timeout after not receiving an ACK
    Several duplicate ACKs in a row
Rate adjustment algorithm
  Modify cwnd
  Probe for bandwidth
  Responding to congestion

## Slide 13: Detection
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
  Missing sequence numbers indicate lost packets
Lost segments detected by sender
  Use timeout to detect missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 14: Implementing Congestion Control
Maintains three variables:
  cwnd: congestion window
  adv_wnd: receiver advertised window
  ssthresh: threshold size (used to update cwnd)
For sending, use: wnd = min(cwnd, adv_wnd)
Two phases of congestion control
  Slow start (cwnd < ssthresh)
    Probe for bottleneck bandwidth
  Congestion avoidance (cwnd >= ssthresh)
    AIMD
Notes: Got to here.

## Slide 15: Slow Start
Upon starting (or restarting) a connection
  cwnd =1
  ssthresh = adv_wnd
  Each time a segment is ACKed, cwnd++
Continues until…
  ssthresh is reached
  Or a packet is lost
Slow Start is not actually slow
  cwnd increases exponentially

## Slide 16: Slow Start Example
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd grows rapidly
Slows down when…
  cwnd >= ssthresh
  Or a packet drops

## Slide 17: Congestion Avoidance
AIMD mode
If cwnd >= ssthresh then each time a segment is ACKed increment cwnd by 1/cwnd (cwnd += 1/cwnd).
So cwnd is increased by one only if all segments have been acknowledged

## Slide 18: Congestion Avoidance Example
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 19: The Big Picture
Time
cwnd
Timeout
Slow Start
Congestion
Avoidance
ssthresh

## Slide 20: The Evolution of TCP
Thus far, we have discussed TCP Tahoe
  Original version of TCP
However, TCP was invented in 1974!
  Today, there are many variants of TCP
Early, popular variant: TCP Reno
  Tahoe features, plus…
  Fast retransmit
  Fast recovery

## Slide 21: TCP Reno: Fast Retransmit
Problem: in Tahoe, if segment is lost, there is a long wait until the RTO
Reno: retransmit after 3 duplicate ACKs
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
2
3
4
4
4
4
3 Duplicate ACKs

## Slide 22: TCP Reno: Fast Recovery
After a fast-retransmit set cwnd to ssthresh/2
  i.e. don’t reset cwnd to 1
  Avoid unnecessary return to slow start
  Prevents expensive timeouts
But when RTO expires still do cwnd = 1
  Return to slow start, same as Tahoe
  Indicates packets aren’t being delivered at all
  i.e. congestion must be really bad

## Slide 23: Fast Retransmit and Fast Recovery
At steady state, cwnd oscillates around the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 24: Many TCP Variants…
Tahoe: the original
  Slow start with AIMD
  Dynamic RTO based on RTT estimate
Reno: fast retransmit and fast recovery
NewReno: improved fast retransmit
  Reduce number of retransmissions
  Window inflation
Vegas: delay-based congestion avoidance
And many, many, many more…

## Slide 25: TCP in the Real World
What are the most popular variants today?
  Key problem: TCP performs poorly on high bandwidth-delay product networks (like the modern Internet)
  Compound TCP (Windows)
    Based on Reno
    Uses two congestion windows: delay based and loss based
    Thus, it uses a compound congestion controller
  TCP CUBIC (Linux)
    Enhancement of BIC (Binary Increase Congestion Control)
    Window size controlled by cubic function
    Parameterized by the time T since the last dropped packet

## Slide 26: High Bandwidth-Delay Product
Key Problem: TCP performs poorly when
  The capacity of the network (bandwidth) is large
  The delay (RTT) of the network is large
  Or, when bandwidth * delay is large
    b * d = maximum amount of in-flight data in the network
    a.k.a. the bandwidth-delay product
Why does TCP perform poorly?
  Slow start and additive increase are slow to converge
  TCP is ACK clocked
    i.e. TCP can only react as quickly as ACKs are received
    Large RTT  ACKs are delayed  TCP is slow to react

## Slide 27: Reno
Low window size resilience to packet loss in High-Speed Network
Packet loss
Time (RTT)
Congestion avoidance
Packet loss
Packet loss
cwnd
Slow start
Packet loss
100,000
10Gbps
50,000
5Gbps
1.4 hours
1.4 hours
1.4 hours
TCP
Slow Increase
cwnd = cwnd + 1
Fast Decrease
cwnd = cwnd * 0.5
Presentation: "Congestion Control on High-Speed Networks”, Injong Rhee, Lisong Xu, Slide 7

## Slide 28: Poor Performance of TCP Reno CC
Bottleneck Bandwidth (Mb/s)
Avg. TCP Utilization
50 flows in both directions
Buffer = BW x Delay
RTT = 80 ms
Round Trip Delay (sec)
Avg. TCP Utilization
50 flows in both directions
Buffer = BW x Delay
BW = 155 Mb/s

## Slide 29: Goals
Fast window growth
  Slow start and additive increase are too slow when bandwidth is large
  Want to converge more quickly
Maintain fairness with other TCP variants
  Window growth cannot be too aggressive
Improve RTT fairness
  TCP Tahoe/Reno flows are not fair when RTTs vary widely
Simple implementation

## Slide 30: Compound TCP Implementation
Default TCP implementation in Windows
Key idea: split cwnd into two separate windows
  Traditional, loss-based window
  New, delay-based window
wnd = min(cwnd + dwnd, adv_wnd)
  cwnd is controlled by AIMD
  dwnd is the delay window
Rules for adjusting dwnd:
  If RTT is increasing, decrease dwnd (dwnd >= 0)
  If RTT is decreasing, increase dwnd
  Increase/decrease are proportional to the rate of change

## Slide 31: Compound TCP Example
Low
RTT
High
RTT
Aggressiveness corresponds to changes in RTT
Advantages: fast ramp up, more fair to flows with different RTTs
Disadvantage: must estimate RTT, which is very challenging
Time
cwnd
Timeout
Slow Start
Timeout
Slower cwnd growth
Faster cwnd growth

## Slide 32: TCP CUBIC Implementation
Default TCP implementation in Linux
Replace AIMD with cubic function
Solve RTT un-fairness
  B  a constant fraction for multiplicative increase
  T  time since last packet drop
  W_max  cwnd when last packet dropped

## Slide 33: CUBIC Algorithm
ACK received
  C is a scaling factor
  t is the elapsed time from the last window reduction
  Wmax is the window size just before the last window reduction
  K is updated at the time of last lost event
Recovery
  Update K with:
  Update Wmax with:
  β is a constant multiplication decrease factor
cwnd cannot be less than
as to keep the growth rate the same as standard TCP in short RTT networks.

## Slide 34: TCP CUBIC Example
Less wasted bandwidth due to fast ramp up
Stable region and slow acceleration help maintain fairness
  Fast ramp up is more aggressive than additive increase
  To be fair to Tahoe/Reno, CUBIC needs to be less aggressive
Time
cwnd
Timeout
Slow Start
CUBIC Function
cwndmax
Fast ramp up
Stable
Region
Slowly accelerate to probe for bandwidth

## Slide 35: Simulations of CUBIC Flows
CUBIC
CUBIC
Reno
Reno

## Slide 36: Deploying TCP Variants
TCP assumes all flows employ TCP-like congestion control
  TCP-friendly or TCP-compatible
  Violated by UDP :(
If new congestion control algorithms are developed, they must be TCP-friendly
Be wary of unforeseen interactions
  Variants work well with others like themselves
  Different variants competing for resources may trigger unfair, pathological behavior

## Slide 37: Issues with TCP
The vast majority of Internet traffic is TCP
However, many issues with the protocol
  Lack of fairness
  Synchronization of flows
  Poor performance with small flows
  Really poor performance on wireless networks

## Slide 38: Fairness
Problem: TCP throughput depends on RTT
1 Mbps
1 Mbps
1 Mbps
1 Mbps
1 Mbps
100 ms
1000 ms
ACK clocking makes TCP inherently unfair
Possible solution: maintain a separate delay window
  Implemented by Microsoft’s Compound TCP

## Slide 39: Synchronization of Flows
Ideal bandwidth sharing
cwnd
cwnd
cwnd
Oscillating, but high overall utilization
In reality, flows synchronize
One flow causes all flows to drop packets
Periodic lulls of low utilization

## Slide 40: Small Flows
Problem: TCP is biased against short flows
  1 RTT wasted for connection setup (SYN, SYN/ACK)
  cwnd always starts at 1
Vast majority of Internet traffic is short flows
  Mostly HTTP transfers, <200KB
  Most TCP flows never leave slow start!
Proposed solutions (driven by Google):
  Increase initial cwnd to 10
  TCP Fast Open: use cryptographic hashes to identify receivers, eliminate the need for three-way handshake

## Slide 41: Wireless Networks
Problem: Tahoe and Reno assume loss = congestion
  True on the WAN, bit errors are very rare
  False on wireless, interference is very common
TCP throughput ~ 1/sqrt(drop rate)
  Even a few interference drops can kill performance
Possible solutions:
  Break layering, push data link info up to TCP
  Use delay-based congestion detection (TCP Vegas)
  Explicit congestion notification (ECN)

## Slide 42: TCP Perspectives
Cerf/Kahn
  Provide flow control
  Congestion handled by retransmission
Jacobson / Karels
  Need to avoid congestion
  RTT estimates critical
  Queuing theory can help
Winstein/Balakrishnan
  TCP is maximizing an objective function
    Fairness/efficiency
    Throughput/delay
  Let a learning program pick the best fit for your environment