## Slide 1: Overview of EU LBT and its Effectiveness for Coexistence of LAA LTE and Wi-Fi
Date: 2014-11-4
Authors:

## Slide 2: Background
3GPP has recently approved a study item on licensed-assisted access (LAA) LTE (See [1]).
LAA LTE will make use of unlicensed spectrum as a secondary component carrier for transmission of data plane traffic only
LAA LTE, in the absence of new coexistence mechanisms, can potentially create new challenges for legacy Wi-Fi leading to unfair spectrum sharing scenarios (See, for example, contribution 802.19-14/0037r2 [2] and [3]).
One solution that has been proposed by the 3GPP SI is the use of listen-before-talk (LBT) mechanism for LAA devices. LBT is currently imposed as regulatory requirements in certain regions of the world.
  See [4] for details of LBT regulations in Europe
In this contribution, we argue that the use of LBT, as prescribed by the European regulators and in its current form, does not sufficiently address the unfairness problem between LAA LTE and Wi-Fi.

## Slide 3: Overview of LBT
LBT is a regulatory policy for channel access in unlicensed bands enforced in certain regions of world (See [4] for LBT regulations in Europe)
  In [4], different LBT requirements are defined for “Frame based equipment” and “Load based equipment”
  Load based equipment (LBE): Equipment where the transmit/receive structure is not fixed in time but demand-driven
  Frame based equipment (FBE): equipment where the transmit/receive structure is not directly demand-driven but has fixed timing

## Slide 4: FBE LBT
Apply clear channel assessment (CCA) using energy detect for channel observation time ≥ 20 μs
If clear, transmit with a channel occupancy time (no need to re-evaluate during this period) between [1ms 10ms]. Follow by an idle time > 5% of channel occupancy time. Perform a new CCA.
If not clear, remain quiet for the next fixed frame period.
CCA is performed once every fixed frame period
  Channel access opportunity is only once every fixed frame period
Apply CCA for a duration ≥ 20 μs
Clear
Yes
No
Occupy the channel
for [1ms 10ms]
Remain idle for > 5% of channel occupancy time
Remain quite for the next fixed frame period
Yes
No

## Slide 5: LBE LBT
Apply clear channel assessment (CCA) using energy detect for channel observation time ≥ 20 μs
If clear, transmit with a channel occupancy time (no need to re-evaluate during this period) for less than 13/32*q ms where q is a fixed number in the range [4 32].
  Channel occupancy time: [1.625 13] ms.
If not clear perform an extended CCA.
  Extended CCA: Channel is observed for the duration of (N*channel observation time). N is a random number selected in the range of [1 q].
Similar to Wi-Fi, CCA is performed continuously without abiding any frame boundaries.
Apply CCA for channel observation time ≥ 20 μs
Clear
Yes
No
Occupy the channel
for < 13/32*q ms
Perform Extended CCA with observation time=
N* CCA observation time
N random chosen from [1 q]
q fixed between 4 and 32
Clear
Yes
No
Yes
No
Yes
No

## Slide 6: LBT for LAA LTE
In FBE LBT, channel access is possible only once during one fixed frame period.
The extended CCA in LBE LBT is similar to the backoff mechanism in Wi-Fi. Similar to Wi-Fi, CCA is performed continuously.
  LBE LBT based channel access is a proposed functional requirement for LAA LTE (See [5])
However, unlike Wi-Fi, the backoff mechanism in LBE LBT is not exponential. The contention window size is always within the [20 20×q] μs range and does not increase after a collision.
  The consequence is, as shown in simulation results, the collision rate and channel access probability degrades significantly for large number of users.

## Slide 7: Simulation Assumptions
All nodes are within CCA range of each other
Single 20 MHz channel is used
Full buffer traffic
802.11 EDCA channel access for Wi-Fi STAs
  All traffic is mapped to Best Effort access category (AIFS = 3, CWmin = 15)
LBE LBT for LAA users
  q=10, 25 and 32 are considered.
All nodes are stationary
Monte Carlo model with 1,000,000 TXOPs evaluated per data point

## Slide 8: Simulation Results: Probability of Collision
2X nodes in 3 scenarios:
  All nodes are Wi-Fi STAs
  All nodes are LAA users
  X Wi-Fi STAs and X LAA users
q= 10, 25 or 32
When all nodes are Wi-Fi STAs, probability of collision increases much more slowly with number of STAs.
  The exponential backoff in Wi-Fi increases the contention window size and hence avoids linear increase in collision probability when number of STAs increases.
Coexistence with LAA users increases the probability of collision for Wi-Fi STAs for large number of nodes.
  For large q values (q>CWmin), the collision probability decreases for small number of nodes.

## Slide 9: Simulation Results: Probability of Successful Channel Access
When all nodes belong to a single network, the EDCA in Wi-Fi leads to larger probability of successful channel access than the LBE LBT in LAA.
  The gap is larger for larger number of nodes or for smaller q
Wi-Fi STAs coexisting with LAA users will have much lower probability of successful channel access compared to LAA users.
  Wi-Fi STAs will be unfairly impacted due to the presence of LAA users
Wi-Fi STAs coexisting with LAA users will have zero chance of successful channel access for large number of nodes.

## Slide 10: Conclusions
While the Listen Before Talk, as a general approach, can be a good basis for coexistence of LAA LTE and Wi-Fi, the LBE LBT in its current form, as introduced by European regulations, is still unfair to Wi-Fi.
  LBE based LAA nodes will impact Wi-Fi nodes (in terms collision rate and probability of successful channel access) more than similar Wi-Fi nodes on the same carrier
    This is not compliant with the objectives as listed in 3GPP LAA LTE SI (See objective 2 in [1])
One major reason is the use of non-exponential backoff in LBE LBT.
To make the LBT in LAA LTE in par with Wi-Fi channel access, the extended CCA must be modified to incorporate exponential backoff. In addition rigorous optimization of the LBT parameters must be performed to ensure fairness to both Wi-Fi and LAA users.

## Slide 11: References
  [1] 3GPP RP-141664, Study of Licensed Assisted Access Using LTE
  [2] 802.19-14/0037r2: Impact of LTE in Unlicensed Spectrum on WiFi
  [3] A. Babaei, J. Andreoli-Fang and B. Hamzeh, “On the Impact of LTE-U on Wi-Fi Performance,” in Proceedings of IEEE PIMRC 2014 conference.
  [4] ETSI EN 301 893 V1.7.1
  [5] 3GPP R1-144000, Solutions for required functionalities and design targets.